## Slide 1
GIS APPLICATIONS IN TELECOMMUNICATIONS
Day 1: See the Network. Own the Map.
GIS Fundamentals · Coordinate Systems · Geodatabase Design · ER Cardinality From National ISP Core → Fiber → Homes | Towers → Sectors
5-Day Intensive Training | Version 3.0 | ArcGIS Pro Companion to Day1_GIS_Fundamentals_Geodatabase_Manual_v3

## Slide 2
Hook: Why are we here?
A network without geography is just a spreadsheet of outages waiting to happen
Dropped calls
happen somewhere — GIS finds the where
Churn risk
clusters in places — GIS targets retention
Fiber builds
follow routes & cabinets — GIS designs hierarchy
New towers
need coverage + backhaul — GIS supports siting
Day 1 promise: by this afternoon you can design the database relationships that keep ISP inventory truthful — from national core to the living-room ONT.

## Slide 3
Today’s Learning Objectives
What “good” looks like at 16:00
Define GIS and its telecom value in one clear sentence
Identify vector types (point/line/polygon) and when to use raster
Explain GCS vs PCS and when projection is mandatory
Build a File Geodatabase with Feature Dataset + Feature Classes
Assign correct cardinality (1:1, 1:M, M:N) in an ER diagram
Model ISP Core → Hub → OLT → FDH → Splitter → Home and Tower → Sector
Day 1 · GIS Fundamentals · MetroTel Telecom Training v3

## Slide 4
Day 1 Agenda
Theory that sticks + labs that prove it
09:00
Hook + GIS for telecom
09:40
Lab 1: GIS anatomy
11:00
Lab 2: CRS & XY data
13:15
Lab 3: GDB + ER cardinality
15:00
Lab 4: Prove 1:M in data
15:45
Quiz + preview Day 2

## Slide 5
What is GIS? (Definition Slide)
Memorize these definitions
Geographic Information System (GIS)
A system to capture, store, query, analyze, and visualize data that has a location — both WHERE and WHAT.
Spatial data
Information with geometry referenced to a coordinate system (points, lines, polygons, rasters).
Attribute data
The descriptive table behind geometry (IDs, status, height, technology, capacity).
Feature
One real-world object as geometry + attributes (one tower, one fiber cable, one home).
Layer
A map/analysis collection of similar features (Towers layer, Fiber layer, Districts layer).
Day 1 · Strong definitions drive strong analysis

## Slide 6
GIS Components You Will Touch Today
GIS is not “just mapping software” — it is an operational system
Hardware & software: your laptop + ArcGIS Pro (and later ArcGIS Online on Day 5)
Data: synthetic MetroTel ISP hierarchy (and optional real open data)
People & methods: RF/transmission/GIS roles using shared location truth
Analysis: select, join, buffer, relate — beginnings of telecom decision GIS
Visualization: symbology that makes hierarchy readable at a glance
Day 1 · GIS Fundamentals · MetroTel Telecom Training v3

## Slide 7
Vector vs Raster — Choose the right weapon
Telecom uses both; Day 1 focuses on vector networks
VECTOR
• Points: towers, homes, cabinets
• Lines: fiber, microwave paths
• Polygons: districts, compounds
• Best for assets & networks
• Exact coordinates + rich attributes
RASTER
• Grid of cells/pixels
• Each cell has a value
• DEM elevation, coverage RSRP
• Best for continuous surfaces
• Day 2/4 use these heavily

## Slide 8
Coordinate Systems — Definitions that prevent costly mistakes
Memorize these definitions
Geographic CRS (GCS)
Latitude/longitude on a datum (e.g., WGS84). Units = degrees. Great for GPS exchange & storage.
Projected CRS (PCS)
Flattened coordinates in meters/feet (e.g., UTM). Required for distance, buffer, area, density.
Datum
The Earth model behind coordinates. Mixing datums without transformation shifts your towers.
Define Projection
Writes CRS metadata when coordinates are already correct but unlabeled. Does NOT convert values.
Project (tool)
Mathematically converts coordinates from one CRS to another. Use this before meter-based analysis.
Day 1 · Strong definitions drive strong analysis

## Slide 9
Geodatabase Building Blocks
Memorize these definitions
File Geodatabase (.gdb)
Esri spatial database container for feature classes, tables, domains, relationship classes, topologies.
Feature Dataset
Group of feature classes sharing one spatial reference (put ISP network layers together).
Feature Class
Homogeneous features with same geometry type & schema (Towers points, Fiber lines).
Domain
Controlled allowed values (STATUS = Active/Planned). Protects data quality.
Relationship Class
GDB object storing/enforcing relationships and cardinality between tables/feature classes.
Day 1 · Strong definitions drive strong analysis

## Slide 10
Cardinality — The rule that keeps inventory honest
How many of A relate to how many of B?
1 : 1
One-to-one
Each A ↔ one B
Customer ↔ Primary Account (simplified training model)
1 : M
One-to-many
One A → many B
Splitter → many Homes Tower → many Sectors
M : N
Many-to-many
Many A ↔ many B
Towers ↔ Landlords (needs bridge table)
Foreign Key rule: in 1:M, store the parent ID on the child table (Homes.SPLITTER_ID, Sectors.TOWER_ID).

## Slide 11
ER + Cardinality Map — National ISP Fiber & Mobile Access
All hierarchy links below are 1:M (one parent serves many children). FK lives on the child.
ISP Core POP
National backbone
1:M
Regional Hub
Province/region
1:M
OLT / Exchange
GPON headend
1:M
FDH Cabinet
Street cabinet
1:M
Splitter
1:8 / 1:16
1:M
Homes / ONT
Many homes per splitter
Fiber cable feature class connects these nodes (FROM_NODE → TO_NODE). Parent_ID on each child node stores hierarchy. Example: FDH.PARENT_ID = OLT-01.
Mobile / Wireless side (also 1:M)
Backhaul Node
Hub / OLT
1:M
Tower / BTS Site
Rooftop or greenfield
1:M
Sectors / Carriers
Azimuth + 3G/4G tech
Spatial 1:M District → many Towers
How to read & implement this ER
1) Each box = Entity / Feature Class 2) Each “1:M” = one parent row to many child rows 3) Put Foreign Key on the MANY side (child) 4) M:N (Tower ↔ Landlord) needs a bridge table 5) Day 1 lab data implements this exact MetroTel hierarchy for practice selections & joins Device chain to memorize: ISP Core → Regional Hub → OLT → FDH → Splitter → Home/ONT

## Slide 12
Foreign Keys in practice (1:M)
The child table carries the parent’s ID
SPLITTER (Parent — 1)
NODE_ID (PK) SPL-01 SPL-02 SPL-03 One splitter row...
HOMES (Child — Many)
HOME_ID (PK) | SPLITTER_ID (FK) HOME-101 | SPL-01 HOME-102 | SPL-01 HOME-103 | SPL-01 ... Many home rows point to one splitter
1:M

## Slide 13
Why telecom needs a Geodatabase (not loose files)
One spatial reference for the whole access network feature dataset
Relationship classes document cardinality for new staff and contractors
Domains stop “Actve/active/ACTIVE” status chaos
Topology/connectivity later (Day 4) depends on clean schema today
Executive dashboards (Day 5) inherit trustworthy keys and joins
Day 1 · GIS Fundamentals · MetroTel Telecom Training v3

## Slide 14
Hands-on Labs Today
Same MetroTel story in four labs
Lab 1
GIS anatomy
Nodes + fiber on the map
Lab 2
CRS & XY
Towers/homes in UTM meters
Lab 3
GDB + ER
Design cardinality properly
Lab 4
Prove it
1:M selections & joins

## Slide 15
Day 1 Data Package (Synthetic MetroTel)
No confidential customer PII — safe classroom package
ISP_NetworkNodes.csv — Core, Hubs, OLTs, FDHs, Splitters with PARENT_ID
FiberCables.geojson — backbone/aggregation/feeder/distribution lines
Homes_ONT.csv — homes with SPLITTER_ID (child side of 1:M)
Towers.csv + Sectors.csv — tower/sector 1:M wireless model
Cardinality_Rules_ER.csv — official relationship rules for the ER workshop
Optional real data later: HDX boundaries, OSM, regulator site lists
Day 1 · GIS Fundamentals · MetroTel Telecom Training v3

## Slide 16
Trap doors (avoid these on Day 1)
Instructors: pause and quiz here
X Buffering in WGS84 degrees
OK Project to UTM/meters first
X Using Define Projection to “convert” CRS
OK Use the Project tool to convert
X Putting FK on the parent in 1:M
OK FK belongs on the child/many side
X Modeling M:N without a bridge table
OK Create an intermediate table
X Shapefile spaghetti folders
OK Use a Feature Dataset in a GDB

## Slide 17
Rapid Fire Quiz
Answers are in the Day 1 Manual section 10
Define GIS in ≤20 words
Vector or raster for fiber cables?
GCS or PCS for a 500 m tower buffer?
Cardinality of Splitter → Homes? Where is the FK?
Cardinality of Tower → Sector?
Name the chain: ISP Core → ? → ? → ? → ? → Home
Day 1 · GIS Fundamentals · MetroTel Telecom Training v3

## Slide 18
Looking ahead — Your 5-day journey
Day 1 is the foundation everything else stands on
Day 1
Fundamentals + GDB/ER
TODAY
Day 2
Coverage & site selection
Spatial Analyst
Day 3
Geo-marketing & churn
Hot spots
Day 4
Fiber & microwave LOS
Networks
Day 5
AGOL dashboard & story
Executive view

## Slide 19
If you can model cardinality, you can trust the network inventory.
From national ISP core to the home ONT — and from tower to sector — Day 1 gives you the language and the database design discipline.
Open the Manual v3 → start Lab 1 Day1_GIS_Fundamentals_Geodatabase_Manual_v3.docx