## Slide 1
GIS Application in Telecom
Day 1 — Concepts, Data & Geodatabase Design
Introduction to GIS — Concepts, Components & Data Fundamentals Geodatabase Design — Feature Classes, Feature Datasets & Relationship Classes
Outcome: Solid GIS terminology + ability to design a relational geodatabase and assign correct cardinality between telecom entities Version 3.1 | ArcGIS Pro | MetroTel Training Scenario

## Slide 2
Hook: Why Day 1 decides the rest of the program
Without shared GIS language and correct database design, Days 2–5 collapse
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 2 / 37
Coverage maps
need correct CRS & layers
Customer analytics
need clean joins & keys
Fiber / microwave design
need relationships & topology
Executive dashboards
need trustworthy schema
Today you will speak GIS fluently and design the ISP data model from Core POP to Homes — and Tower to Sector.

## Slide 3
Day 1 Curriculum Outcomes
Mapped exactly to the 5-day program plan
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 3 / 37
A
GIS Concepts
What GIS is, why location matters, telecom applications
B
Components
People, data, software, methods, visualization as a system
C
Data Fundamentals
Vector/raster, feature types, attributes, metadata quality
D
Coordinate Systems
GCS vs PCS, datum, define vs project, when meters matter
E
Geodatabase Design
Feature classes, feature datasets, domains, relationship classes
F
Cardinality & ER
1:1, 1:M, M:N — design from real ISP/tower datasets

## Slide 4
Presentation + Lab Flow
Use this deck for teaching; Manual v3 for step-by-step labs
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 4 / 37
1
Concepts & terminology
2
Components & applications
3
Data types & fundamentals
4
Coordinate systems
5
Geodatabase architecture
6
ER + cardinality workshop
7
Labs & Day 1 close

## Slide 5
SECTION 01
Introduction to GIS — Concepts
Build a rock-solid definition before touching tools

## Slide 6
01 · Concepts
Core GIS Terminology
Strong definitions — learn these cold
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 6 / 37
Geographic Information System (GIS)
A system used to capture, store, manage, analyze, and visualize data that is linked to locations on Earth — answering WHERE and WHAT together.
Geographic Information Science
The science behind spatial data, uncertainty, cartography, and spatial analysis methods that GIS software implements.
Spatial data
Any dataset with geometry or location coordinates referenced to a coordinate system.
Attribute data
Non-geometry descriptors of features stored in tables (IDs, status, capacity, technology, owner).
Feature
One real-world object represented as geometry + attributes (one tower, one cable, one district, one home).

## Slide 7
01 · Concepts
More Essential Terms
Strong definitions — learn these cold
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 7 / 37
Layer
A display/analysis unit containing features of one theme (Towers, Fiber, Districts).
Basemap
Reference background (streets/imagery) providing context; usually not the analysis layer.
Map vs Layout
Map = interactive data view; Layout = composed printable/PDF output with legend/scale/north arrow.
Query / Selection
Filtering features by attributes or location (Select by Attribute / Select by Location).
Spatial analysis
Deriving new information from location relationships (buffer, overlay, density, network, suitability).

## Slide 8
01 · Concepts
GIS Applications in Telecom
Why every RF, transmission, marketing, and NOC team needs location
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 8 / 37
Network inventory
Where are OLTs, cabinets, splitters, towers, sectors?
Coverage planning
Where is service strong/weak? Where to add sites?
Geo-marketing
Where are high-ARPU / high-churn customers?
Fiber & microwave design
Which route/LOS connects demand to capacity?
Outage impact
Which customers/assets are affected by a cut?
Executive reporting
Where should money and crews go next?

## Slide 9
SECTION 02
GIS Components
GIS is a system — not only software

## Slide 10
02 · Components
The Five GIS Components
All five must work together for telecom GIS success
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 10 / 37
1. Hardware
Laptops, servers, GPS, field tablets
2. Software
ArcGIS Pro, ArcMap, AGOL, extensions
3. Data
Sites, fiber, customers, DEM, boundaries
4. People
RF, transmission, GIS, marketing, NOC
5. Methods
Standards, QA, workflows, cardinality rules

## Slide 11
02 · Components
Software Stack Used in This Program
Know the platform landscape early
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 11 / 37
Day 1–4 primary: ArcGIS Pro (Catalog, Map, Analysis tools)
Day 4 network option: Utility Network in ArcGIS Pro (Geometric Network is ArcMap legacy; read-only in Pro)
Day 5: ArcGIS Online — Web Maps, Dashboards, StoryMaps
Extensions you will meet later: Spatial Analyst, 3D Analyst
Day 1 focus: Catalog/GDB design + Map visualization + CRS tools

## Slide 12
SECTION 03
Data Fundamentals
Geometry types, attributes, and data quality

## Slide 13
03 · Data Fundamentals
Vector Data Types (Telecom examples)
Match geometry to the real-world object
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 13 / 37
Point
Towers, homes/ONT, cabinets, splitters, core POP
Line / Polyline
Fiber cables, microwave links, trench routes, roads
Polygon
Districts, compounds, coverage polygons, building footprints

## Slide 14
03 · Data Fundamentals
Raster Data Fundamentals
Continuous surfaces used heavily from Day 2 onward
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 14 / 37
What a raster is
• Matrix of cells (pixels) in rows/columns
• Each cell stores one value
• Cell size = spatial resolution
• Good for elevation, slope, coverage strength
• Not ideal as primary inventory for discrete assets
Telecom raster examples
• DEM / DSM for microwave LOS (Day 4)
• RSRP / coverage prediction surfaces (Day 2)
• Population density grids (Day 3)
• Suitability surfaces (Days 2–3)
• Viewshed outputs (Day 4)

## Slide 15
03 · Data Fundamentals
Attributes, Tables & Data Quality
Strong definitions — learn these cold
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 15 / 37
Attribute table
Tabular view of feature properties; each row = one feature; each column = one field.
Primary Key (PK)
Unique identifier field (TOWER_ID, HOME_ID, NODE_ID). Required for trustworthy relationships.
Foreign Key (FK)
Field storing another table’s PK to create a link (Homes.SPLITTER_ID).
Metadata
Data about data: source, date, CRS, accuracy, owner. Protects institutional memory.
Data quality dimensions
Completeness, accuracy, consistency, currency, uniqueness — all matter in telecom inventory.

## Slide 16
SECTION 04
Coordinate Systems
The most expensive Day-1 mistake is usually CRS

## Slide 17
04 · Coordinate Systems
Coordinate System Definitions
Strong definitions — learn these cold
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 17 / 37
Geographic Coordinate System (GCS)
Locations as latitude/longitude on a spheroid/datum (e.g., WGS 1984). Units = degrees.
Projected Coordinate System (PCS)
Flattened map grid in linear units (meters/feet), e.g., UTM Zone. Needed for distance/area/buffer.
Datum
Reference model of Earth. Changing datum without transformation shifts features.
Define Projection
Assigns CRS metadata when coordinates are already correct. Does not convert values.
Project tool
Converts coordinates from one CRS to another. Use before meter-based analysis.

## Slide 18
04 · Coordinate Systems
GCS vs PCS — Decision Rule
Simple rule students can repeat tomorrow
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 18 / 37
Use GCS (WGS84) when…
• Exchanging GPS / survey / CSV XY data
• Storing global datasets
• Publishing to some web basemaps
• Latitude/longitude is the source format
Use PCS (UTM meters) when…
• Buffering towers (e.g., 500 m)
• Measuring fiber route length
• Calculating area / density
• Day 2–4 Spatial Analyst workflows

## Slide 19
04 · Coordinate Systems
CRS Trap Doors
Instructors: quiz this before lunch
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 19 / 37
Never buffer in degrees and pretend the result is meters
Define Projection ≠ Project (labeling vs converting)
Mixed datums without transformation = silent location shift
Feature Dataset forces one shared CRS — design that intentionally
Day 1 lab: load WGS84 XY, then Project to UTM for analysis

## Slide 20
SECTION 05
Geodatabase Design
Feature Classes · Feature Datasets · Relationship Classes

## Slide 21
05 · Geodatabase Design
Geodatabase Architecture — Definitions
Strong definitions — learn these cold
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 21 / 37
Geodatabase (GDB)
Esri’s spatial database container for feature classes, tables, domains, subtypes, relationship classes, topologies, and networks.
File Geodatabase
Local .gdb folder format used throughout this training for project work.
Feature Class
A collection of features with the same geometry type and attribute schema (e.g., Towers as points).
Feature Dataset
A container inside a GDB that groups related feature classes under one spatial reference.
Object Class / Table
Non-spatial table stored in the GDB (e.g., Sectors, ServicePlans).

## Slide 22
05 · Geodatabase Design
Quality & Structure Objects
Strong definitions — learn these cold
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 22 / 37
Domain
Allowed values or ranges for a field (STATUS = Active / Planned / On Air). Improves consistency.
Subtype
Categories inside one feature class with different defaults/domains (TowerType = Rooftop vs Greenfield).
Relationship Class
GDB object that stores/enforces relationships between two classes and defines cardinality.
Topology
Rules about shared geometry (connect, cover, no overlap) — foundation for network integrity.
Schema
The designed structure of datasets, fields, keys, and relationships — your “data constitution.”

## Slide 23
05 · Geodatabase Design
Feature Class vs Feature Dataset vs Relationship Class
The three design objects students must separate clearly
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 23 / 37
Feature Class
What it is
One theme, one geometry type
Example
Towers (points) FiberCables (lines) Districts (polygons)
Feature Dataset
What it is
Family of related FCs sharing one CRS
Example
FD_ISP_Network contains nodes + cables + homes
Relationship Class
What it is
Formal link + cardinality between two classes
Example
RC_Splitter_Homes (1:M)

## Slide 24
05 · Geodatabase Design
Design Pattern for Day 1 MetroTel GDB
This is the practical skill outcome of Day 1
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 24 / 37
Create File GDB: MetroTel_Day1.gdb
Create Feature Dataset FD_ISP_Network (projected UTM CRS)
Load Feature Classes: ISP_Nodes, FiberCables, Homes, Towers, Districts
Keep Sectors as a related table (or point FC) with TOWER_ID FK
Create Relationship Classes for Splitter→Homes and Tower→Sectors (1:M)
Add Domains for STATUS / NODE_TYPE to prevent dirty values

## Slide 25
SECTION 06
Relational Design & Cardinality
Assign the correct relationship between entities

## Slide 26
06 · Cardinality
ER & Cardinality Definitions
Strong definitions — learn these cold
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 26 / 37
Entity
A thing we store as a table/feature class (Tower, Splitter, Home, Hub).
Relationship
A business rule linking entities (Splitter serves Homes; Tower hosts Sectors).
ER Diagram
Entity–Relationship diagram: boxes = entities, lines = relationships, labels = cardinality.
Cardinality
How many instances of A relate to how many of B: 1:1, 1:M, or M:N.
Bridge / Junction table
Required for M:N relationships (e.g., TowerLandlordLease with TOWER_ID + LANDLORD_ID).

## Slide 27
06 · Cardinality
Cardinality Types with Telecom Meaning
Memorize + give one example each
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 27 / 37
1 : 1
One-to-one
Each A relates to one B
Simplified: Customer ↔ Primary Service Account
1 : M
One-to-many
One A relates to many B
Splitter → many Homes Tower → many Sectors OLT → many FDHs
M : N
Many-to-many
Many A relate to many B
Towers ↔ Landlords over lease history (needs bridge table)
Golden rule: in 1:M, store the Foreign Key on the child (MANY) side.

## Slide 28
ER Diagram + Cardinality — ISP Fiber Distribution & Mobile Access
Design from available MetroTel datasets: all main hierarchy links are 1:M; FK on child
ISP Core POP
National backbone
1:M
Regional Hub
Many per country
1:M
OLT / Exchange
GPON headend
1:M
FDH Cabinet
Street cabinet
1:M
Splitter
1:8 / 1:16
1:M
Homes / ONT
Final customer devices
FiberCables connect nodes (FROM_NODE→TO_NODE). Each child stores PARENT_ID. This is how a national ISP distributes fiber optic service down to homes.
Mobile / wireless inventory relationships
Backhaul Node
Hub / OLT
1:M
Tower / Site
Rooftop/greenfield
1:M
Sectors
Many per tower
Also spatial 1:M: District contains many Towers
Assigning cardinality from available datasets (Day 1 skill)
1) Identify entities in the data (nodes, cables, homes, towers, sectors, districts) 2) Ask: one parent to how many children? → usually 1:M in physical networks 3) Place FK on child: Homes.SPLITTER_ID, Sectors.TOWER_ID, Nodes.PARENT_ID, Towers.BACKHAUL_NODE 4) Create Relationship Class in GDB with matching cardinality 5) Validate with Select/Join: one splitter should return many homes

## Slide 29
06 · Cardinality
Implementing 1:M with Foreign Keys
Child table stores parent key — this is non-negotiable
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 29 / 37
PARENT (1) — Splitter
PK: NODE_ID SPL-01 SPL-02 SPL-03 One row per splitter device
CHILD (MANY) — Homes
PK: HOME_ID FK: SPLITTER_ID → NODE_ID HOME-101 | SPL-01 HOME-102 | SPL-01 HOME-103 | SPL-01 ... Many homes served by one splitter
1:M

## Slide 30
06 · Cardinality
Creating a Relationship Class (concept → ArcGIS)
This is the formal GDB implementation of your ER diagram
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 30 / 37
Origin class = parent (Splitter / Tower)
Destination class = child (Homes / Sectors)
Cardinality = One to Many (1:M)
Primary key = parent ID field; Foreign key = child ID field
Optional messaging / composite vs simple based on delete rules
Test: select origin feature → related destination rows appear

## Slide 31
SECTION 07
From Concepts to Practice
Manual labs prove every definition

## Slide 32
07 · Practice
Day 1 Labs (Manual v3)
Concepts become skills only when proven in data
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 32 / 37
Lab 1
GIS anatomy
Map nodes/fiber; click feature ↔ table
Lab 2
Data + CRS
XY points; project to UTM; buffer meters
Lab 3
GDB design
Feature Dataset/Classes; ER + cardinality
Lab 4
Prove relations
1:M selections & joins on real fields

## Slide 33
07 · Practice
Datasets Supporting Concept Learning
All included in Day1 package
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 33 / 37
ISP_NetworkNodes.csv — hierarchy with PARENT_ID (Core→Hub→OLT→FDH→Splitter)
FiberCables.geojson — physical links between nodes
Homes_ONT.csv — child side of Splitter 1:M
Towers.csv + Sectors.csv — Tower 1:M Sectors + backhaul link
Cardinality_Rules_ER.csv — ready-made relationship rule sheet for workshop
Districts.geojson — polygon context for spatial containment discussion

## Slide 34
07 · Practice
Knowledge Check — Can students do this?
If yes, Day 1 outcomes are met
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 34 / 37
□ Define GIS, feature, layer, attribute, vector, raster in one sentence each
□ Name the five GIS components and one telecom example each
□ State when to use GCS vs PCS and Define Projection vs Project
□ Explain Feature Class vs Feature Dataset vs Relationship Class
□ Draw ER for ISP Core→…→Home and label every link 1:M
□ Say where the FK belongs for Tower→Sector and Splitter→Home
□ Create a File GDB + Feature Dataset and load Day 1 layers

## Slide 35
Bridge to Days 2–5
Day 1 language and schema power everything next
Day 1 · GIS Concepts, Components, Data Fundamentals & Geodatabase Design · v3.1 · 35 / 37
Day 2
Coverage & sites
uses towers/sectors + CRS
Day 3
Geo-marketing
uses joins/keys + zones
Day 4
Fiber & microwave
uses relationships/networks
Day 5
ArcGIS Online story
uses clean published schema

## Slide 36
Day 1 standard: speak GIS clearly, design the geodatabase correctly, assign cardinality without guessing.
ISP Core → Hub → OLT → FDH → Splitter → Home Backhaul → Tower → Sectors
Next: open Manual v3 and start Lab 1 Day1_GIS_Fundamentals_Geodatabase_Manual_v3.docx Presentation file: Day1_GIS_Telecom_Concepts_Presentation_v3.pptx

## Slide 37
Instructor copy — text corrections highlighted in this deck
Yellow highlight on slides = wording that was corrected. Review these before delivery.
Slide Correction
Slide 1: GIS APPLICATIONS IN TELECOMMUNICATIONS
→ GIS Application in Telecom
Why: Title slide heading
Slide 1: Day 1 Presentation
→ Day 1 — Concepts, Data & Geodatabase Design
Why: Title slide — clearer session name
Slide 2: Fiber/MW design
→ Fiber / microwave design
Why: Spell out MW
Slide 8: GIS Applications in Telecommunications
→ GIS Applications in Telecom
Why: Section title consistency
Slide 8: Fiber & MW
→ Fiber & microwave
Why: Spell out MW
Slide 11: Day 4 classic network option: ArcMap Geometric Network / Utility Network Analyst
→ Day 4 network option: Utility Network in ArcGIS Pro (Geometric Network is ArcMap legacy; read-only in Pro)
Why: ArcMap is retired; Geometric Network is not editable in Pro
Slide 18: Day 2–4 spatial analyst workflows
→ Day 2–4 Spatial Analyst workflows
Why: Product name capitalization
Slide 22: STATUS = Active/Planned/OnAir
→ STATUS = Active / Planned / On Air
Why: Spacing and On Air
Slide 35: Fiber & MW
→ Fiber & microwave
Why: Spell out MW
Slide 35: AGOL story
→ ArcGIS Online story
Why: Spell out AGOL
Day 1 · Instructor corrections log · v3.1 · Remove this slide before presenting · 37 / 37